## Slide 1
Gamma Shielding Material Analysis: A Comparative Study

## Slide 2
Objective and Background
Objective
Compare gamma shielding properties of Lead, HY80, and 30MnB5.
Identify the best material or hybrid design for nuclear submarine shielding.
Background
Submarines require lightweight yet effective gamma radiation shielding.
Cesium-137 (Eγ=0.662 MeV) is used as the gamma source.

## Slide 3
Experimental Setup
1
Gamma Source
Cesium-137 (Eγ=0.662 MeV).
2
Materials Tested
Lead (Pb): High density (11.34 g/cm3).
HY80 Steel: Medium density (7.87 g/cm3).
30MnB5 Steel: Medium density (7.835 g/cm3).
3
Data Analyzed
Peak intensity, FWHM, and Compton edge for thicknesses from 0 cm to 25 cm.
4
Tools Used
GEANT4 simulations and gamma spectroscopy.

## Slide 4
Key Metrics Evaluated
Peak Intensity
Indicates attenuation efficiency.
FWHM
Measures scattering contributions.
Compton Edge
Highlights energy redistribution due to interactions.

## Slide 5
Results: Peak Intensity
Observation
Lead shows the sharpest drop in peak intensity with increasing thickness, indicating superior attenuation.
HY80 and 30MnB5 require greater thickness for comparable attenuation.
Visualization
Peak Intensity vs. Thickness graph.

## Slide 6
Results: FWHM
Observation
Lead maintains a narrow and stable FWHM across thicknesses, suggesting minimal scattering.
HY80 and 30MnB5 exhibit broader FWHM, reflecting increased scattering.
Visualization
FWHM vs. Thickness graph.

## Slide 7
Gaussian Profiles
Lead
Sharp Gaussian peaks, minimal scattering.
HY80 & 30MnB5
Broader Gaussian curves, scattering contributions.

## Slide 8
Weight vs. Performance
1
Lead
Most efficient gamma shield, heaviest.
2
HY80 & 30MnB5
Better weight-to-performance ratios, require increased thickness.

## Slide 9
Recommendations and Conclusion
1
Hybrid Designs
Combine HY80 (outer layer) with 30MnB5 (inner layer).
2
Testing Conditions
Simulate high-pressure, high-temperature, and corrosive environments.
3
Optimization
Use simulation tools to refine material combinations.

## Slide 11
Questions?